## Slide 1: Sector Level Mappinng FTL
Computer engineering , Sungkyunkwan Univ.
Oh Gihwan, Han Gyuhwa , Hong Gyeonghwan
Jasmine Open-SSD Project Tutorial 2
- Sector Level Mapping FTL
Notes: Good Evening, I am presenter, Hong Gyeonghwan.
We ran this project, sector level mapping FTL based on OpenSSD Platform, for a month.
안녕하세요, 저는 발표자 홍경환입니다.
우리는 한 달 동안 OpenSSD 플랫폼을 기반으로 Sector Level Mapping FTL을 만드는 프로젝트를 진행했습니다.

## Slide 2: Index
Sector Level Mapping
Consideration : How to Fill Merge Buffer?
Write module for sector level mapping
Read module for sector level mapping
Experiments
Conclusion
Reference
Notes: I will talk about sector level mapping, and considerations about it.
And I will talk about write module, read module for sector level mapping.
Then I will talk about experiments, and conclusion.
Sector Level Mapping과 이에 대한 고찰에 대해 먼저 말씀드리겠습니다.
그 후 Sector Level Mapping에 필요한 write module, read module, 이에 대한 실험과 결론까지 말씀드리겠습니다.

## Slide 3: Sector Level Mapping
LSN | PSN
<W, 100, 10>
<W, 2, 20>
<R, 3, 10>
<W, 100, 20>
.
.
<W, 20, 60>
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
Flash Memory Page
Sector Mapping
Table
Merge Buffer
Notes: We made two main data structures for sector level mapping.
One is sector mapping table, the other is merge buffer.
Sector mapping table is the array of PSNs, physical sector number.
And LSN is index of this array.
So when some requests are coming to FTL, LSN is translated to PSN through Sector Mapping Table.
PSN will be used for physical access to NAND.
Merge buffer is the buffer merging incoming sectors to a page.
It is because the basic writing unit is page, not sector.
When write commands comes to FTL, sectors are stacked in this buffer.
And when merge buffer is full, it programs these pages to NAND.
우리는 sector level mapping을 위해 두 가지 주요 자료 구조들을 구현했습니다.
하나는 sector mapping table이며, 또 다른 하나는 merge buffer입니다.
Sector mapping table은 physical sector number, PSN들로 이루어진 배열을 말합니다. 또한 LSN이 이 배열의 index입니다.
FTL로 어떤 request가 오면, LSN이 sector mapping table을 통해 PSN으로 번역됩니다.
이 PSN은 나중에 NAND를 물리적으로 접근하기 위해 사용됩니다.
Merge buffer는 들어오는 섹터를 한 페이지로 합쳐주는 버퍼입니다.
NAND에 ‘쓰기’를 하는 기본 단위는 섹터가 아니라 페이지이기 때문이죠.
FTL에 쓰기 명령이 들어오면, 섹터들은 이 버퍼에 쌓이게 됩니다.
Merge buffer가 가득차면, FTL은 안에 있는 페이지를 NAND로 program하게 됩니다.

## Slide 4: Write module (1/4)
LSN | PSN
20 | 0x80...
21 | 0x80...
22 | 0x80…
..... | 
100 | 0x80...
101 | 0x80...
<W, 100, 10>
<W, 2, 20>
<W, 100, 20>
.
.
<W, 20, 60>
100 | 101 | ............. | 21 | 22
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
Flash Memory Page
Merge Buffer
Sector Mapping
Table
Notes: It is write module.
In example, write request meaning “write ten sectors starting at hundredth sector” come to FTL.
Then it translates LSN to PSN through sector mapping table.
After getting PSN, it distinguish if the sector is in merge buffer or NAND flash.
If the most significant bit of PSN is one, it means required sector is on merge buffer.
In this case, it copies the sector’s contents into merge buffer at the same position.
If it is zero, It means the sector is on NAND flash.
In this case, it put the sector into merge buffer, then update PSN in sector mapping table.
It sets most significant bit of PSN as one.
Then it repeats for ten sectors.
(You may have a question how can it do if merge buffer is full.)
If one page in the merge buffer, FTL flushes the page to NAND, and updates PSNs.
write 모듈입니다.
예를 들어, 100번째 섹터부터 10개의 섹터를 쓰라는 write request가 FTL에 왔다고 합시다.
그러면 LSN이 sector mapping table을 통해 PSN으로 번역됩니다.
그 다음에 PSN을 얻으면, 이 섹터가 NAND에 있는지 머지 버퍼에 있는지를 구별합니다.
PSN의 맨 처음 비트(MSB)가 1이면, 머지 버퍼에 섹터가 있다는 뜻이고
0이면, NAND에 있다는 뜻입니다.
섹터가 머지 버퍼에 들어가고, sector mapping table에 있는 PSN을 갱신합니다.
즉 PSN의 MSB를 1로 설정합니다.
이 동작을 여기서는 10개의 섹터에 대해 반복하여 실행합니다.
만약 머지 버퍼가 가득 찬다면, FTL이 머지 버퍼에있는 페이지를 NAND로 flush하고, PSN들을 갱신합니다.

## Slide 5: Considerations : How to Fill Merge Buffer?
Fill one merge buffer in order of incoming
  1-Buffer : Just put sectors to merge buffer
  Multi-copy : Just put sectors, but put sectors with succeeding LBAs at once
Distribute sectors to several merge buffers by banks
  Dynamic : Distribute sectors to merge buffers in order of incoming
  Static : Distribute sectors to merge buffers, but bank number is fixed by LBA
Notes: Then we considered about how to fill merge buffer.
It is main consideration of our project.
There is so big difference in performance according to those methods.
It is so important.
There is two large ways.
First large way is ~~, Second large way is ~~.
First large way can be divided to ~~ and ~~
  One-Buffer method is ~~
  Multi-copy method is ~~
  Second large way can be divided to ~~and ~~.
  Dynamic method is ~~.
  Static method is ~~.
  그 다음에

## Slide 6: Write module (2/4)
<W, 100, 10>
<W, 2, 20>
<W, 100, 20>
.
.
<W, 20, 60>
21 |  | ............. |  | 
22 |  | ............. |  | 
Flash Memory Page
Merge Buffer
100 |  | ............. |  | 
101 |  | ............. |  | 
Sector Mapping
Table
LSN | PSN
20 | 0x80...
21 | 0x80...
22 | 0x80…
..... | 
100 | 0x80...
101 | 0x80...
Notes: In Dynamic methods.
When write requests come, FTL distributes sectors to merge buffers in order of incoming, by bank.
The number of merge buffer is same as the number of bank.
The bank number of each sector is determined by LSN.
If merge buffers are full, flush these all merge buffers to NAND.

## Slide 7: Write module (3/4)
<W, 100, 10>
<W, 2, 20>
<R, 3, 10>
<W, 100, 20>
.
.
<W, 20, 60>
 |  | ............. |  | 
 |  | ............. |  | 
Flash Memory Page
Merge Buffer
100 | 101 | ............. | 21 | 22
 |  | ............. |  | 
Sector Mapping
Table
LSN | PSN
20 | 0x80...
21 | 0x80...
22 | 0x80…
..... | 
100 | 0x80...
101 | 0x80...
Notes: In 1-buffer methods.
When write request comes, FTL fills merge buffers in order of incoming.
It puts sectors into one merge buffer.
If one merge buffer is full, flush it to NAND.

## Slide 8: Write module (4/4)
<W, 100, 10>
<W, 2, 20>
<R, 3, 10>
<W, 100, 20>
.
.
<W, 20, 60>
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
100 | 101 | ........ | 21 | 22
Flash Memory Page
Merge Buffer
Sector Mapping
Table
LSN | PSN
20 | 0x00...
21 | 0x00…
22 | 0x00…
..... | 
100 | 0x00…
101 | 0x00…
Notes: After all sectors are written to NAND, they are in each bank according to buffer number.
And the most significant bit of PSN becomes 0.
It means this sector is in NAND, not merge buffer.

## Slide 9: Read module
<R, 100, 10>
<R, 2, 20>
<R, 3, 10>
<R, 100, 20>
.
.
<R, 20, 60>
100 | 101 | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
2 | 3 | ........ | 21 | 22
Flash Memory Page
Merge Buffer
Sector Mapping
Table
LSN | PSN
20 | 0x00...
21 | 0x00...
22 | 0x00…
..... | 
100 | 0x80...
101 | 0x80...
Notes: It is read module.
In example, read request meaning “read ten sectors starting at hundredth sector” come to FTL.
Then it translates LSN to PSN through sector mapping table.
After getting PSN, it distinguish if the sector is on merge buffer or NAND flash.
If the most significant bit of PSN is one, it means required sector is on merge buffer.
In this case, FTL reads required sector from merge buffer.
If it is zero, It means the sector is on NAND flash.
In this case, FTL reads required sector from NAND flash.
Then it repeats for ten sectors.

## Slide 10: Experiments
Environment
  Application : Iometer
  Transfer size
    Random test : 512 Bytes, 1 KB , 2KB , 4KB
    Sequential test : 128 KB
Target FTL
  Tutorial
  Greedy
  Static Sector mapping
  Dynamic Sector mapping
  1 buffer Sector mapping
  Multi copy Sector mapping
Notes: Then we did experiments.
We used IO-meter application for measuring performance of our FTL.
In random test, transfer size is ~~
In sequential test, transfer size is ~~
Target FTL is six. ~~ exist in OpenSSD.
~~ is what we made.

## Slide 11: Experiments results
IOPS
Notes: In 64GB random write experiment.
1_buffer, dynamic, static, multi_copy are sector level mapping FTLs, but tutorial 1, greedy are page level mapping FTLs.
Sector mapping FTLs have greater random write IOPS than page mapping FTLs.
It is because in small random write, page mapping FTLs waste more spaces than sector mapping FTLs.
(But especially, Multi-copy FTL puts succeeding sectors at once, so the performance drop is shown by transfer size increase.)

## Slide 12: Experiments results
MB/s
Notes: In 64GB sequential write and read experiment,
Sector mapping FTLs have worse sequential performance than page mapping FTLs.
It is because in sequential write and read, mapping table access overhead of sector mapping FTLs is more than page mapping FTLs.
(Especially, dynamic and static FTL have grater read performance than 1-buffer and multi-copy FTL. It is because dynamic and static FTL distribute pages by bank, but 1-buffer and multi-copy dose not.)

## Slide 13: Experiments results
Random Write Test ( Average of four tests )
Sequential Read/Write Test ( Average of four tests )
x10
x8
Notes: In random write test, these are IOPS of each FTLs.
In 512Bytes, four sector level FTLs shown about 20000 IOPS, but two page level FTLs shown about only 2400, 1600 IOPS.
It is 10 times difference.
Sector level FTLs has greater random write performance than page level FTLs.
It is because in small random write, page mapping FTLs waste more spaces than sector mapping FTLs.
In sequential test, write speed and read speed of sector level FTLs are about 8 times slower than page level FTLs.

## Slide 14: Experiments results
Test Without Map Table Caching ( Average of four tests )
Test with Map Table Caching ( Average of four tests )
x 1/50 ~ 1/20
Cache Miss Rate : about 90% (Random Write)
Notes: Prior experiment was the test without map table caching.
But in test with map table caching, miss rate becomes about 90%, so the map table caching overhead increase total overhead so much.
Therefore, the performance decreases about 1 over 50 times!

## Slide 15: Conclusion
Small random write performance of sector mapping is GREAT!
Sequential read/write performance of sector mapping is LOW…
Shrinking mapping table OVERHEAD is important.
Notes: These are our conclusion.
Small random write performance of sector mapping is GREAT!
Sequential read/write performance of sector mapping is LOW…
Shrinking mapping table OVERHEAD is important.

## Slide 16: References
DFTL: a flash translation layer employing demand-based selective caching of page-level address mappings / 저자: Aayush GuptaKim, Bhuvan UrgaonkarYoungjae
OpenSSD Project - www.openssd-project.org.
The Jasmine OpenSSD Platform: FTL Developer's Guide –http://www.openssd-project.org/
The Jasmine OpenSSD Platform: Technical Reference Manual - http://www.openssd-project.org/
Notes: These are our references.

## Slide 17: Q & A
Notes: There is any question?