## Slide 1: Sector Level Mappinng FTL
Computer engineering , Sungkyunkwan Univ.
Oh Gihwan, Han Gyuhwa , Hong Gyeonghwan
Jasmine Open-SSD Project Tutorial 2
- Sector Level Mapping FTL
Notes: Good Evening, I am presenter, Hong Gyeonghwan.
We ran this project, sector level mapping FTL based on OpenSSD Platform, for a month.

## Slide 2: Index
Sector Level Mapping
Consideration : How to Fill Merge Buffer?
Write module for sector level mapping
Read module for sector level mapping
Experiments
Conclusion
Reference
Notes: I will talk about sector level mapping, considerations about it.
And I will talk about write module, read module for sector level mapping.
Then I will talk about experiments, and conclusion.

## Slide 3: Sector Level Mapping
LSN | PSN
<W, 100, 10>
<W, 2, 20>
<R, 3, 10>
<W, 100, 20>
.
.
<W, 20, 60>
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
Flash Memory Page
Sector Mapping
Table
Merge Buffer
Notes: We made two main data structure for sector level mapping.
One is sector mapping table, the other is merge buffer.
Sector mapping table is the array of PSNs, physical sector number.
And LSN is index of this array.
So when LSN is coming to FTL, it is translated to PSN through Sector Mapping Table.
PSN will be used for physical access to NAND.
Merge buffer is the buffer merging sectors to a page.
It is because the basic writing unit is page, not sector.
When write commands comes to FTL, sectors are stacked in this buffer.
And when merge buffer is full, program these data page to NAND.

## Slide 4: Write module (1/4)
LSN | PSN
100 | 0x80...
101 | 0x80...
..... | 
20 | 0x80...
21 | 0x80...
22 | 0x80...
<W, 100, 10>
<W, 2, 20>
<W, 100, 20>
.
.
<W, 20, 60>
100 | 101 | ............. | 21 | 22
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
Flash Memory Page
Merge Buffer
Sector Mapping
Table
Notes: It is write module.
In example, write request meaning “write ten sectors starting at hundredth sector” come to FTL.
Then it translates LSN to PSN through sector mapping table.
After getting PSN, it distinguish if the sector is in merge buffer or NAND flash.
If the most significant bit of PSN is one, it means required sector is on merge buffer.
In this case, it copies the sector’s contents into merge buffer at the same position.
If it is zero, It means the sector is on NAND flash.
In this case, it put the sector into merge buffer, then update PSN in sector mapping table.
It sets most significant bit of PSN as one.
Then it repeats for ten sectors.
(You may have a question how can it do if merge buffer is full.)
If one page in the merge buffer, FTL flushes the page to NAND, and updates PSNs.

## Slide 5: Considerations : How to Fill Merge Buffer?
Fill one merge buffer in order of incoming
  1-Buffer : Just put sectors to merge buffer
  Multi-copy : Just put sectors, but put sectors with succeeding LBAs at once
Distribute sectors to several merge buffers by banks
  Dynamic : Distribute sectors to merge buffers in order of incoming
  Static : Distribute sectors to merge buffers, but bank number is fixed by LBA
Notes: Then we considered about how to fill merge buffer.
It is main consideration of our project.
There is so big difference in performance according to those methods.
It is so important.
There is two large ways.
First large way is ~~, Second large way is ~~.
First large way can be divided to ~~ and ~~
  One-Buffer method is ~~
  Multi-copy method is ~~
  Second large way can be divided to ~~and ~~.
  Dynamic method is ~~.
  Static method is ~~.

## Slide 6: Write module (2/4)
LSN | PSN
100 | 0x80...
101 | 0x80...
..... | 
20 | 0x80...
21 | 0x80...
22 | 0x80...
<W, 100, 10>
<W, 2, 20>
<W, 100, 20>
.
.
<W, 20, 60>
21 |  | ............. |  | 
22 |  | ............. |  | 
Flash Memory Page
Merge Buffer
100 |  | ............. |  | 
101 |  | ............. |  | 
Sector Mapping
Table
Notes: In Dynamic methods.
When write requests come, FTL distributes sectors to merge buffers in order of incoming, by bank.
The number of merge buffer is same as the number of bank.
The bank number of each sector is determined by LSN.
If merge buffers are full, flush these all merge buffers to NAND.

## Slide 7: Write module (3/4)
LSN | PSN
100 | 0x80...
101 | 0x80...
..... | 
20 | 0x80...
21 | 0x80...
22 | 0x80...
<W, 100, 10>
<W, 2, 20>
<R, 3, 10>
<W, 100, 20>
.
.
<W, 20, 60>
 |  | ............. |  | 
 |  | ............. |  | 
Flash Memory Page
Merge Buffer
100 | 101 | ............. | 21 | 22
 |  | ............. |  | 
Sector Mapping
Table
Notes: In 1-buffer methods.
When write request comes, FTL fills merge buffers in order of incoming.
It puts sectors into one merge buffer.
If one merge buffer is full, flush it to NAND.

## Slide 8: Write module (4/4)
LSN | PSN
100 | 0x00...
101 | 0x00...
..... | 
20 | 0x00...
21 | 0x00...
22 | 0x00...
<W, 100, 10>
<W, 2, 20>
<R, 3, 10>
<W, 100, 20>
.
.
<W, 20, 60>
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
100 | 101 | ........ | 21 | 22
Flash Memory Page
Merge Buffer
Sector Mapping
Table
Notes: After all sectors are written to NAND, they are in each bank according to buffer number.
And the most significant bit of PSN becomes 0.
It means this sector is in NAND, not merge buffer.

## Slide 9: Read module
LSN | PSN
100 | 0x80...
101 | 0x80...
..... | 
20 | 0x00...
21 | 0x00...
22 | 0x00...
<R, 100, 10>
<R, 2, 20>
<R, 3, 10>
<R, 100, 20>
.
.
<R, 20, 60>
100 | 101 | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
 |  | ............. |  | 
2 | 3 | ........ | 21 | 22
Flash Memory Page
Merge Buffer
Sector Mapping
Table
Notes: It is read module.
In example, read request meaning “read ten sectors starting at hundredth sector” come to FTL.
Then it translates LSN to PSN through sector mapping table.
After getting PSN, it distinguish if the sector is on merge buffer or NAND flash.
If the most significant bit of PSN is one, it means required sector is on merge buffer.
In this case, FTL reads required sector from merge buffer.
If it is zero, It means the sector is on NAND flash.
In this case, FTL reads required sector from NAND flash.
Then it repeats for ten sectors.

## Slide 10: Experiments
Environment
  Application : Iometer
  Transfer size
    Random test : 512 Bytes, 1 KB , 2KB , 4KB
    Sequential test : 128 KB
Target FTL
  Tutorial
  Greedy
  Static Sector mapping
  Dynamic Sector mapping
  1 buffer Sector mapping
  Multi copy Sector mapping
Notes: Then we did experiments.
We used IO-meter application for measuring performance of our FTL.
In random test, transfer size is ~~
In sequential test, transfer size is ~~
Target FTL is six. ~~ exist in OpenSSD.
~~ is what we made.

## Slide 11: Experiments results
Random Write test ( Average of four tests )
Sequential Read/Write test ( Average of four tests )
x10
x8
Notes: In random write test, these are IOPS of each FTLs.
1_buffer, dynamic, static, multi_copy is sector level mapping FTLs, but tutorial 1, greedy is page level mapping FTLs.
In 512Bytes, four sector level FTLs shown about 20000 IOPS, but two page level FTLs shown about only 2400, 1600 IOPS.
It is 10 times difference.
Sector level FTLs has greater random write performance than page level FTLs.
In sequential test, write speed and read speed of sector level FTLs are about 8 times slower than page level FTLs.

## Slide 12: Experiments results
IOPS
Notes: In 64GB random write experiment.
Sector mapping FTLs has greater random write IOPS than page mapping FTLs.
It is because in small random write, page mapping FTLs waste more spaces than sector mapping FTLs.
(But especially, Multi-copy FTL puts succeeding sectors at once, so the performance drop is shown by transfer size increase.)

## Slide 13: Experiments results
MB/s
Notes: In 64GB sequential write and read experiment,
Sector mapping FTLs has worse sequential performance than page mapping FTLs.
It is because in sequential write and read, mapping table access overhead of sector mapping FTLs is more than page mapping FTLs.
(Especially, dynamic and static FTLs can )

## Slide 14: Conclusion
Small random write performance of sector mapping is GREAT!
Sequential read/write performance of sector mapping is LOW…
Shrinking mapping table OVERHEAD is important.
Notes: These are our conclusion.
Small random write performance of sector mapping is GREAT!
Sequential read/write performance of sector mapping is LOW…
Shrinking mapping table OVERHEAD is important.

## Slide 15: References
DFTL: a flash translation layer employing demand-based selective caching of page-level address mappings / 저자: Aayush GuptaKim, Bhuvan UrgaonkarYoungjae
OpenSSD Project - www.openssd-project.org.
The Jasmine OpenSSD Platform: FTL Developer's Guide –http://www.openssd-project.org/
The Jasmine OpenSSD Platform: Technical Reference Manual - http://www.openssd-project.org/
Notes: These are our references.

## Slide 16: Q & A
Notes: There is any question?